## Slide 1
An Introduction to Water Resources Management in Colorado and the West
John Tracy, Director of the Colorado Water Center
Presented at the Water Literate Leaders of Northern Colorado
September 13, 2023

## Slide 2: Topics
How does water move through the environment?
How much water exists on earth, and how much do we use?
How does Colorado manage its water?
What are Colorado’s water management challenges?

## Slide 3: The Hydrologic Cycle
Water moves in a cycle.
When water is used, it is never created or destroyed
It simply changes its form or is transported to a new location
One groups water use turns into another groups water supply

## Slide 4: How much exists on earth?
Water is found in many forms:
Oceans = 3.53e+20 gallons of water: 96.6%
Lakes = 2.93e+16 gallons of water: 0.008%
Streams = 7.31e+14 gallons of water: 0.0002%
Ice Caps and Glaciers = 6.22e+18 gallons of water: 1.7%
Groundwater = 6.22e+18 gallons of water: 1.7%
Fresh = 2.93e+18 gallons of water: 0.8%
Saline = 3.29e+18 gallons of water: 0.9%
Atmosphere = 3.66e+15 gallons of water: 0.001%
From the USGS

## Slide 5: How rapidly does water move between its forms?
Estimate of flux into and out of water’s forms:
Atmosphere ~ 9.52e+18 gallons per year (2 weeks residence time)
Streams ~ 1.27e+16 gallons per year (3 weeks residence time)
Lakes ~ 1.46e+16 gallons per year (2 years residence time)
Icecaps and Glaciers ~ 6.22e+17 gallons per year (1,000 years residence time)
Groundwater ~ 2.93e+16 gallons per year (100 years residence time)

## Slide 6: How much water do humans use?
On an annual basis, our best current estimate on the amount of water that humans extract from the environment is:
Annual Global Water Use ~ 1.06e+15 gallons per year
Which is Approximately:
1.87% of the flux of all fresh water in lakes, streams, and groundwater;
or
0.011% of the amount of water that cycles through the atmosphere on an annual basis

## Slide 7: What is the Water Situation in the West?
Managing water in Streams, Reservoirs, Canals, Ditches, and Groundwater
Snowpack in Headwaters
Natural Stream
Dam
Reservoir
Ditch
Water Use
Canal
Flow increases as snow melts in early summer, then decreases later in summer
Reservoirs allow balancing flows out over the summer when water is needed
Ditches allow water to be moved from natural stream to where it is needed
Canals allow water that is not needed to be returned to the river
Groundwater

## Slide 8: How does this management change flows?
Clearwater River
above Lewiston
Salmon River before the Snake River
Snake River above the Salmon River
Image From Wikipedia (http://en.wikipedia.org/wiki/Snake_River)
The Snake and Salmon River Example
Over 9 Million Acre-ft of water storage was added to the Snake River above Joseph from the 1900s to the 1980s.
The majority of this storage was for water supply, with additional storage for hydropower generation.
None of this storage was designed to carry water over from year to year.
There are no water storage facilities in the Salmon River Drainage

## Slide 9: How does this management change flows?
The Snake and Salmon River Example
Chart: Relatively Monthly Flow for Snake and Salmon River Drainages
| Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep
Snake River at Joseph | 0.81347 | 0.81347 | 0.95702 | 1.1165 | 1.276 | 1.2122 | 1.3132 | 1.2973 | 1.2548 | 0.61675 | 0.6008 | 0.7284
Salmon River at White Bird | 0.42773 | 0.44398 | 0.40698 | 0.38081 | 0.39795 | 0.49992 | 1.0468 | 2.8786 | 3.4291 | 1.2092 | 0.48368 | 0.39525
Ratio of monthly flow to average flow is:
Peak Snake River Flow: 1.35 to 1.00
Low Snake River Flow: 0.6 to 1.00
Peak Salmon River Flow: 3.50 to 1.00
Low Salmon River Flow: 0.45 to 1.00
Desired effect of river management is to “flatten” the flows to reduce flooding in the high runoff months, and increase water supply in the low runoff months

## Slide 10: What is the Water Situation in Colorado?
Yampa-White River
Arkansas River
Gunnison River
South Platte River
Colorado River
Rio Grande
North Platte River Watershed
Southwest Rivers
From 2023 Colorado Water Plan

## Slide 11: What is the Water Situation in Colorado?
Two Main Types of Groundwater Aquifers
Alluvial Aquifers –
Tend to be near the ground surface and act as extensions of nearby streams
Bedrock Aquifers –
Tend to be well below the ground surface, are not well connected to streams, and are often non-renewable
85% of Colorado’s groundwater is used for irrigated agriculture
18% of Colorado’s population relies on groundwater for their home water supplies
60% of groundwater use is from non-renewable sources

## Slide 12: What is the Water Situation in Colorado?
Colorado has a total of 44 structures that divert water from one watershed to another
The majority of these diversions divert water from the western watersheds of the Continental Divide to the eastern watersheds
The largest diversion is the Redlands Power Canal, which diverts over 500,000 acre-ft per year from the Gunnison to the Colorado River
The largest diversion to the Eastern Watersheds is the Adams Tunnel, which diverts over 200,000 acre-ft per year from the Colorado to South Platte River Watershed

## Slide 13: What is the Water Situation in Colorado?
Irrigated Agricultural Use:
  Extracted = 8,999.64 Mgal/day
  Consumed = 2,651.1 Mgal/day
  Irrigated area = 3,036,930 acres
Municipal Use:
  Extracted = 843.95 Mgal/day
  Consumed (billed) = 636.69 Mgal/day
  Population = 5,170,100 persons
  Per capita use = 163 gallons/person/day
Self-supplied Use:
  Extracted = 35.37 Mgal/day
  Consumed = 35.37 Mgal/day
  Population = 286,474 persons
  Per capita use = 123 gallons/person/day
Colorado’s largest uses are for Irrigated Agriculture and Municipal Purposes (2015 USGS)
Chart: Total Water Extracted ~ 11 Million Acre-ft
| Agriculture | Municipal | Self Supplied
Water Extracted | 10080856.7496 | 945342.153 | 39619.3518
Chart: Total Water Consumed ~ 3.7 Million Acre-ft
| Agriculture | Municipal | Self Supplied
Water Extracted | 2969603.154 | 713181.9366 | 39619.3518

## Slide 14: What are Colorado’s Water Management Challenges? – A Changing Climate
Changing climate leads to:
Increased wildland consumptive use of water;
Alteration of hydrologic patterns;
Less certainty in understanding drought and flood frequencies/magnitudes.

## Slide 15: What are Colorado’s Water Management Challenges? – Demographic Change
Chart: Year
| 1920 | 1930 | 1940 | 1950 | 1960 | 1970 | 1980 | 1990 | 2000 | 2010 | 2020
CO Growth % | 0.20275 | 0.082206 | 0.086538 | 0.16814 | 0.34091 | 0.24859 | 0.34842 | 0.10738 | 0.25455 | 0.22947 | 0.1336
Western Growth % | 0.30085 | 0.33768 | 0.16721 | 0.40403 | 0.3893 | 0.24064 | 0.24052 | 0.22284 | 0.1972 | 0.13845 | 0.092286
US Growth % | 0.14952 | 0.16204 | 0.072808 | 0.14496 | 0.18496 | 0.13323 | 0.11486 | 0.097815 | 0.13152 | 0.097115 | 0.073522
US Population | 92.23 | 106.02 | 123.2 | 132.17 | 151.33 | 179.32 | 203.21 | 226.55 | 248.71 | 281.42 | 308.75 | 331.45
Western US | 7.08 | 9.21 | 12.32 | 14.38 | 20.19 | 28.05 | 34.8 | 43.17 | 52.79 | 63.2 | 71.95 | 78.59
Colorado | 0.799 | 0.961 | 1.04 | 1.13 | 1.32 | 1.77 | 2.21 | 2.98 | 3.3 | 4.14 | 5.09 | 5.77
Population Growth in the US, West, and Colorado
Population Growth leads to:
Increased competition for water resources;
Changes in our relationship with water and the natural environment;
Differing priorities for Hydro-Services.

## Slide 16: Does Colorado Need More Water to Address these Challenges?
Chart: Total Fresh Water Use Trends in the United States
| 1985 | 1990 | 1995 | 2000 | 2005 | 2010
Total Water Use | 395119.85 | 403631.7 | 397400.75 | 404295.23 | 348129.62
Agricultural Water Use | 137240.82 | 137031.06 | 134339.48 | 136803.22 | 128389.15 | 115302.07
Municipal Water Use | 36147.83 | 38139.16 | 39775.4 | 42732.57 | 43544.88 | 41019.88
Thermo-Electric Water Use | 184688.21 | 192472.72 | 187173.68 | 192927.95 | 197014.47 | 158353.27
Population | 238857.47 | 248712.41 | 263209.32 | 281428.63 | 296643.858 | 308745.845
Passed Peak water use in 2005; Agriculture passed peak water use in 2000.

## Slide 17: Does Colorado Need More Water to Address these Challenges?
From US Bureau of Economic Analysis (1960 to 2020)
Chart: Trend in US GDP since 1960
Has Reduced Water Use Impacted our Economic Productivity?
Water Use Plateaued

## Slide 18: Does Colorado Need More Water to Address these Challenges?
Has reduced water use affected our agricultural productivity?
From USDA Economic Research Service (1960 to 2020)
Chart: Trend in US Farm Productivity - Normalized to Year 2015
| 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Trend in US Farm Productivity | 0.43561 | 0.4409 | 0.44489 | 0.46043 | 0.4578 | 0.46989 | 0.4685 | 0.48407 | 0.49139 | 0.50115 | 0.49429 | 0.52782 | 0.53006 | 0.55464 | 0.52507 | 0.56882 | 0.57146 | 0.59836 | 0.606 | 0.64243 | 0.62143 | 0.6764 | 0.68618 | 0.58964 | 0.66978 | 0.69943 | 0.67231 | 0.68051 | 0.64187 | 0.69384 | 0.72716 | 0.73001 | 0.77264 | 0.73521 | 0.82131 | 0.77842 | 0.81572 | 0.8482 | 0.85401 | 0.87374 | 0.87856 | 0.88312 | 0.86514 | 0.88387 | 0.92441 | 0.91233 | 0.90233 | 0.92714 | 0.96099 | 0.97131 | 0.95827 | 0.9617 | 0.96108 | 1.0288 | 1.0063 | 1 | 1.0301 | 1.0239 | 1.0066 | 0.99772
Water Use Plateaued

## Slide 19: Does Colorado Need More Water to Address these Challenges?
The answer that the data is suggesting is that Colorado does not need more water to address its growing population, economy, and changing climate.
This data also suggests that Colorado needs to improve its focus on growing the social, ecological, and economic value we receive from effectively managing our water resources.
Increasing this value of water management will require embracing a holistic, as opposed to incremental, approach to water management.
It will also require creating more a more inclusive and equitable environment for engaging in discussions on the future management of water resources.