## Slide 1: City of Greeley: Water for Municipalities
2023/2024 Water Literate Leaders
December 13, 2023

## Slide 2: Agenda
Introduction
History of Greeley
Greeley W&S Today
Challenges
Planning Ahead
Q&A

## Slide 3: Introduction
Deputy Director of Water Resources at the City of Greeley
  Lead Conservation, High Mountain Reservoir Operations, Non-potable Operations, Water Resource Operations, and Water Resource Planning teams
  25+ staff, $10M+ operating budget, $90M+ 10-year CIP budget
Former Lead/Senior Planner at Denver Water
Englewood, Colorado Water & Sewer Board Member
Education
  Adjunct Faculty Member @ University of Denver
  PhD, Civil Engineering, University of British Columbia
  MBA, University of Illinois
  MS, Environmental Engineering Sciences, Colorado School of Mines
  BS, Environmental Sciences, University of Vermont

## Slide 4: History
Union Colony founded in 1870, location chosen between Cache la Poudre & South Platte Rivers
  Early agriculture revolved around wheat and other dry land crops with German-Russians later introducing potatoes and sugar beets, requiring more water
  Farmers started digging ditches to get the water to their fields citizens were using water from infiltration wells along the river
Residents quickly realized that the water in the Poudre was limited to the wet season and not very good quality by the time it reached the confluence
  Greeley went above Fort Collins at the mouth of Poudre canyon and built a slow sand filter plant (Bellvue)

## Slide 5: Greeley Today

## Slide 6: Source of Supply

## Slide 7: Greeley’s Water & Sewer System
Potable Water Infrastructure
  Bellvue WTP (35 MGD): Started operating in 1907, year-round (baseline) water plant
  Boyd Lake WTP (38 MGD): Started operating in 1964, seasonal (peaking) water plant
  ~500 miles of pipeline, ~29,000 meters, ~3,700 fire hydrants, ~70 million gallons of storage
Non-potable Water Infrastructure
  ~25 miles of piped infrastructure, 40 pump stations, rely on regional ditch infrastructure
  Currently use ~2,000 AF/year, anticipated to be ~7,100 AF/year at buildout
Wastewater Infrastructure
  1 water treatment and reclamation facility (WTRF), treats 7.5 MGD
  360+ miles of collection pipes, 10 lift stations

## Slide 8: Treated Water
Greeley
Colorado
Big Thompson
Cache la Poudre
Boyd WTP
Bellvue WTP
North
Laramie
WTRF
Terry Ranch

## Slide 9: Non-potable System

## Slide 10: Greeley-specific Challenges
Beyond aging infrastructure, regional workforce competition, changing regulatory environment, etc.…

## Slide 11: Infrastructure Footprint

## Slide 12: Long Range Expected Growth Area

## Slide 13: Planning for Uncertainty & Growth
Water Demand Projections
Population Projections

## Slide 14: Impact of Wildfires

## Slide 15: Planning for an uncertain future

## Slide 16
Foundation of collaborative, data-driven planning efforts
  Integrated Water Resources Plan (IWRP)
    Long-range water supply strategy
  Water Efficiency Plan
    Conservation program blueprint
  Technical Master Plans (e.g. Non-potable, Transmission and Distribution)
Formal Master Planning

## Slide 17
Regional collaboration and proactive forest health initiatives
  Board member representative for both Coalition for the Poudre River Watershed (CPRW) and Big Thompson Watershed Coalition
  Stakeholder for Coalition for the Poudre River Watershed Upper Poudre Resiliency Plan and municipal stakeholder in American Forests/USFS reforestation strategy for Arapahoe Roosevelt National Forest
  Partnering on Wildfire Ready Action Plan (WRAP) with Ft. Collins for Upper Poudre watershed and Big Thompson Watershed Health Partnership for Big Thompson watershed
  Participant in Watershed Wildfire Protection Group, Watershed Health Investment Partners, and Cameron Peak Fire Restoration collaborative groups
Post-fire mitigation
  Stabilize sites, minimize erosion & sedimentation, mitigate water quality impacts
  $31M+ spent from Greeley/State/Federal funds, estimating $5M+ from USFS for 2024-2025 USFS-funded projects
Investing in Watershed Health

## Slide 18
Conservation at the Forefront
Indoor and outdoor water efficiency assessments
Rebate and incentive programs
Professional landscape certifications
Life After Lawn, turf replacement program
Garden in a Box program
Online Water Efficiency Tools
  Water Budget Portal
  WaterSmart Portal
  Online Plant Database
Youth, Adult and Teacher Educational Programs
Future income qualified programs

## Slide 19: Terry Ranch (aquifer storage and recovery)
Non-tributary aquifer decreed with 1,200,000 acre-feet of native water
  When available, treated surface water is injected into the aquifer
  During droughts, water is extracted from the aquifer, treated again, and delivered to Greeley
Compliments acquisition strategy

## Slide 20
Formalize data empowerment and tech enablement
Support emerging technologies
  Advanced Metering Infrastructure (AMI) full implementation by 2025
  Geospatial AI for system assessment
  Acoustic leak detection
  Snowpack and canopy health LIDAR
Innovating and Adapting

## Slide 21
Questions?