## Slide 1
April 27, 2023
Efficiency in Irrigated Agriculture
Does It Save Water?
Joel P. Schneekloth
Regional Water Resources Specialist
Colorado Water Center and Extension

## Slide 2: Agriculture in the South Platte Basin
Agriculture uses approximately 86% of the water in the South Platte Basin.
  5 of the top 10 counties are within the South Platte Basin ($3.5 billion)
  854,000 irrigated acres
  80% of Colorado’s population
South Platte is net water short
  Can increase efficiency help solve the problem?

## Slide 3
Of the top 20 counties in Colorado
15 – Eastern Plains
3 – San Luis Valley
2 – Western Slope

## Slide 4: South Platte River
Prior to development
  Raging river from snow melt
  Dry during summer due to lack of snow melt
Beginning of development
  Development of irrigation
    Near river as well as ditches farther from the river
  River began to flow more consistently in summer in regions
    Leads to more irrigation development
Increased Storage in the Alluvial Aquifer
  Rivers are a drainage system for the basin

## Slide 5
Source: Murry-Darling Basin

## Slide 6
Furrow Irrigation Center Pivot

## Slide 7: Water Use in a Water Short Environment
Water Conservation Irrigation Efficiency Actual Consumptive Water Use How does efficiency impact stream flows?

## Slide 8: How the river works
20 cfs 15 cfs 10 cfs 5 cfs
5 cfs 5 cfs 5 cfs
10 cfs 5 cfs 0 cfs 0 cfs
5 cfs 5 cfs ? cfs
Senior water rights – shut off junior rights to get his water

## Slide 9: How the river works
10 cfs 8 cfs 6 cfs 4 cfs
5 cfs 5 cfs 5 cfs
3 cfs return
3 cfs return
3 cfs return
10 cfs 7 cfs 4 cfs 1 cfs
3 cfs 3 cfs 3 cfs

## Slide 10: How the river works
20 cfs 17 cfs 14 cfs 11 cfs
3 cfs 3 cfs 3 cfs
Low Efficiency
High Efficiency
20 cfs 18 cfs 16 cfs 14 cfs
5 cfs 5 cfs 5 cfs
3 cfs return
3 cfs return
3 cfs return

## Slide 11: Return Flows
Return flows are what built irrigation within the basin
  Stabilized flows during the summer when flows were low
  Retiming of water to low flow times
Water Supply
  1.4 million acre-ft of native water supplies
  0.4 million acre-ft of trans basin diversion
Annual diversions on South Platte
  4 million acre-ft

## Slide 12: Efficiency – On Farm vs Basin
On Farm Efficiency has many benefits
  Greater yields
  Reduced leaching of nutrients
  Labor savings vs furrow irrigation
Downfall
  Reduced return flows into system
  Need for greater storage
    Expensive
  Greater issues with salinity
As changes to greater efficiency happen, changes to the system will need to be made
  Storage

## Slide 13
The Consumptive Use Conundrum: Economics vs Water Savings
Questions?